## Slide 1: Sprint 8
drifts analysis summary
gwloggeR update

## Slide 2: Agenda
gwloggeR update
  Test framework
  Issue #47
Summary drift analysis
  Multi comparison (one vs. all) vs Reference comparison (one vs KNMI)
  Barometer overview: best to worst
Barometer altitude analysis
Next step proposals
  detect_drifts() function

## Slide 3: gwloggeR
Update

## Slide 4: gwloggeR update Testing framework
For each function and each INBO/Geotech file:
Result
Image
Metadata
 Testing framework makes sure that the package functions produce the same results as before, and only fix that what needs to be fixed.

## Slide 5: gwloggeR update Issue #47
Fix of issue #47 has only effect on this specific case.

## Slide 6: Summary drift analysis
Multi- and reference comparison analysis
Barometer overview: best to worst

## Slide 7: Multi comparison: good One barometer vs all the rest
Notes: Zie voor theorie naar slides sprint 7.
Je verwacht een stationair rode lijn: vast gemiddelde met ruis errond.

## Slide 8: Multi comparison: bad One barometer vs all the rest
Notes: De gemiddelde van de rode lijn is hier niet stationair, maar oscilleert en daalt zelfs.

## Slide 9: Multi comparison: KNMI (Westdorpe) KNMI barometer assessment based on multi comparison analysis
No drift and SD analysis suggests performance of an average INBO barometer.

## Slide 10: Reference comparison: good One barometer vs KNMI reference barometer

## Slide 11: Reference comparison: bad One barometer vs KNMI reference barometer

## Slide 12: Multi or reference comparison? Which analysis method is better?
Pretty much the same results
  A possibly better question is: which one is more practical?
Need one good barometer.
Need lots of barometers.

## Slide 13: Overview Multi comparison overview based on IQR range

## Slide 14: Seasonality in timeseries? Cf. WMO-No. 8: Guide to Instruments
“Most instruments measure temperature to compensate its effect.”
Electronic barometers (Ch 3.2, p119)
  Capacitive sensors: diaphragm changing the capacitor  temperature dependent
  Piezoresistive  can be made temperature independent and immune to hysteresis
  Cylindrical resonator  temperature dependent
  Aneroid (= “without fluid”) displacement: vs hydrostatic gauges  temperature dependent
“In order to maintain the acceptable performance of a barometer, the calibration corrections applied to the readings must be checked at relatively frequent intervals, for example, starting annually, for early detection and replacement of defective instruments.”

## Slide 15: Barometer altitude analysis

## Slide 16: Barometer altitude analysis
Altitude from barometric formula () assumes at MSL: 1013.25 hPa at 15 °C
In Belgium we use the for which the MSL doesn’t necessarily correspond to the MSL. (i.e. as the “0-calibration” point is different)
Two questions:
  Each place has a fixed average pressure? (i.e. such as 1013.25hPa at MSL?)
  Can we assume the following relationship?
Notes: Note that in the barometric formula the assumption is that MSL is at 1013.25 hPa and 15 °C, In Belgium we use TAW as the MSL. So although we all use the same pressure reduction techniques, the "0-calibration point" is not necessarily the same.
ABF main purpose is to explain the differences in pressure in function of the altitude: where you place the “0-point” seems less important (although there is a slight impact since the 0-point temperature will have an impact on the laps rate.)

## Slide 17: Barometer altitude analysis Fixed average pressure can be measured correctly?

## Slide 18: Barometer altitude analysis
Slope is 0,86 (1 within 99%) while intercept is -32.6.

## Slide 19: Barometer altitude analysis
Not enough data: no evidence that broken.
Barometer offset problem?
Relative error: amount of data taken into consideration.

## Slide 20: Barometer altitude analysis
logger N altitude.m.bf RASTERVALU altitude.m.rel_err
1: barodata/BAOL015X_72527.csv 4420 -84.582470 28.29 4.495663
2: barodata/BAOL109X_P4024.csv 4477 78.818297 60.00 3.525451
3: barodata/BAOL004X_77561.csv 7667 -60.749429 35.72 3.467790
4: barodata/BAOL849X_A9771.csv 958 97.650572 4.45 3.068416 ***
5: barodata/BAOL029X_R6549.csv 3054 -72.348491 30.65 3.038848
6: barodata/BAOL019X_77560.csv 7425 -22.046760 70.25 2.936357
7: barodata/BAOL014X_R6519.csv 3478 -51.858903 25.82 2.395642
8: barodata/BAOL845X_P2_15488.csv 2167 -80.559779 22.67 2.279869 ***
9: barodata/BAOL027X_77554.csv 6065 -10.962409 69.11 2.225562
10: barodata/BAOL070X_B9393.csv 775 75.014820 6.59 2.220084 ***
11: barodata/BAOL088X_B5548.csv 841 64.536759 7.39 2.068103 ***
12: barodata/BAOL012X_D1095.csv 3355 7.058513 1.96 1.973851
13: barodata/BAOL093X_78679.csv 4396 -11.125500 62.70 1.910527 ***
14: barodata/BAOL064X_59976.csv 4967 -12.756265 59.96 1.867836
15: barodata/BAOL054X_F6598.csv 2165 104.657061 94.64 1.847558
16: barodata/BAOL071X_H4445.csv 1539 49.146993 22.42 1.794395 ***
17: barodata/BAOL009X_78681.csv 4023 -37.837886 27.89 1.721346
18: barodata/BAOL001X_D0939.csv 5391 7.197382 15.63 1.552928
Notes: So although these barometers do not drift, their median pressures seem to be way off from what we expect, so I would advise to double-check them.

## Slide 21: Next steps
detect_drift()

## Slide 22: Next steps detect_drift()
Based on “Multi or Reference comparison” analysis.
Output should divide the timeseries in FALSE and TRUE (= drift)

## Slide 23: Next steps detect_drift()
Interface
  detect_drift(x)
    Probably the least precise: only information supplied is the time series of a barometer.
  detect_drift(x, reference)
    Based on reference comparison analysis:
      Reference should be a good non-drifting barometer.
      Reference should span the whole time-frame of x.
    The larger the distance, the less accurate the results. (cf. “each 100km the error is 2 cmH2O due to distance”)
  detect_drift(x, other, [altitude])
    Based on multi comparison analysis:
      Need most of the other barometers to make a comparison and thus detect drift.
    Probably the most precise (not yet confirmed).

## Slide 24: Next steps detect_drift()
Most of the analysis up till now was based on the variance of differences between one barometer vs. all/reference.
  Hysteresis is indistinguishable from drift based on variance alone:
Notes: Similar variance numbers

## Slide 25: Next steps detect_drift()
Based on “Multi or Reference comparison” analysis.

## Slide 26: Next steps detect_drift()
And then there is the occasional trouble:
Might cause trouble for an algorithm.

## Slide 27: Next steps detect_drift()
Detecting up- or down-ward movement is tricky and in the starting phase, will mainly depend on how much new data on has.
  When should the algorithm say that this one started drifting?
I think the algorithm should first detect seasonality, and then later a drift.
Notes: Similar variance numbers

## Slide 28: Next steps detect_drift()
A first tryout on the algorithm that can detect drifts?
  Design
  Implementation
  Assessment
Analysis on the seasonality pattern:
  Specific frequency (i.e. yearly) or multiple frequencies?
Notes: Similar variance numbers

## Slide 29: The End

## Slide 30: Sprint 7
Analysis: drifts in air pressure

## Slide 31: Agenda
Air pressure data analysis
  Altitude
  Temperature
  Humidity
Barometer drift detection
  Pairwise difference model
  Multi difference model
Next steps
Questions

## Slide 32: Air pressure modeling
Theory and data analysis

## Slide 33: Air pressure
Model for pressure based on ideal gas law:
And Bernoulli’s equation:
and depend on:
  Altitude
depends on:
  Temperature
  Humidity
depends on:
  Flow

## Slide 34: Altitude Barometric formula
Around sea-level, an increase of 100 m in altitude corresponds to a decrease of 12 cmH2O in air pressure.
Notes: https://en.wikipedia.org/wiki/Barometric_formula#Derivation

## Slide 35: Altitude Barometric formula
Notes: https://en.wikipedia.org/wiki/Barometric_formula

## Slide 36: Altitude Barometric formula
Notes: https://en.wikipedia.org/wiki/Barometric_formula

## Slide 37: Barometer altitude
Notes: Can be extracted with e.g. Google Elevation API for comparison.

## Slide 38: Temperature Data analysis
Temperature distribution of all barometers.

## Slide 39: Temperature Data analysis
Raw data: BAOL016X_W1666.csv and BAOL050X_56819.csv excluded.
Notes: Blue line is the median regression.

## Slide 40: Temperature Data analysis
Notes: Blue line is the median regression. Yellow is OLS: might be influenced by outliers.

## Slide 41: Temperature Theory
Both and are unknown (and interdependent)
We have only one equation
For discussion, see here
Theoretical effect of local temperature change on air pressure unknown. More research needed.

## Slide 42: Temperature Data analysis
The bulge? Seasonal?
Notes: Blue line is the median regression.

## Slide 43: Humidity Data analysis
Bulge due to high humidity?

## Slide 44: Humidity Theory
Theory assumes known and uses Dalton's law of partial pressures for density calculations.
(molar mass) is also impacted, again too many unknowns, so approximations are used. See here, note 14.
Theoretical effect of humidity on air pressure unknown. More research needed.

## Slide 45: Summary
Altitude
  Effect is significant: 12 cmH2O per 100m.
Temperature: effect unknown
  Data analysis suggests 0,07 cmH2O drop per 1 °C. Over the observed range [-10, 50] °C this amounts to 4 cmH2O change.
Humidity: effect unknown
  Seasonality analysis shows humidity has no impact on mean air pressure.
  Humidity might be causing more lower pressure observations during non-summer time. (i.e. the bulge around 5 °C)

## Slide 46: Barometer drift analysis
Theory and results

## Slide 47: Ideal situation: 2 barometers side by side
and
Subtract yields:
Notes: Neem aan dat epsilons normal verdeeld zijn.

## Slide 48: Pairwise comparison Two barometers close to each other.
At 11m and 13m altitude? So differences are white noise around 0 cmH2O.
Notes: At 11m and 13m altitude.

## Slide 49: Situation: 2 barometers at a distance
and
Subtract yields:

## Slide 50: Pairwise comparison Two barometers close to each other.
At -27m and -23m altitude? So differences are white noise around 0 cmH2O.

## Slide 51: Pairwise comparison SD (MAD) of pressure differences (cmH2O) vs distance (km): Q50 and Q10

## Slide 52: Situation: 2 barometers at a distance and different altitude
and
Subtract yields:

## Slide 53: Pairwise comparison Two barometers far from each other.
At -32m and 13m altitude? So differences are white noise around 6 cmH20.

## Slide 54: Pairwise comparison Two barometers while one drifting: high SD
Very high SD due to drift.
Notes: Als nodig, dan kan ik die plots nog verbeteren… want in analyse 02 is matching niet optimaal.

## Slide 55: Pairwise comparison Problems

## Slide 56: Pairwise comparison Conclusion
They do not tell us which one is drifting,
If they both drift the same way, we do not even see it.

## Slide 57: Situation: multiple barometers at a distance and different altitude
and
Subtract yields:
Notes: Als hier nu een paar Yi fout zijn, maar de meeste Yi juist zijn, dan zouden die paar foute geen al te grote

## Slide 58: Multi comparison One barometer vs all the rest

## Slide 59: Multi comparison One barometer vs all the rest

## Slide 60: Multi comparison One barometer vs all the rest

## Slide 61: Multi comparison One barometer vs all the rest

## Slide 62: Multi comparison One barometer vs all the rest

## Slide 63: Multi comparison One barometer vs all the rest
Temperature pattern in blue: positively correlated.

## Slide 64: Multi comparison One barometer vs all the rest
You never see barometers first oscillating and then stabilizing.
Notes: Feit dat ze altijd naar het einde toe oscilleren weerlegt een mogelijk argument dat de baro’s in andere tijdenlijk andere weeromstandigheden staan.

## Slide 65: Multi comparison One barometer vs all the rest

## Slide 66: Multi comparison One barometer vs all the rest
Temperature pattern in blue: negatively correlated.

## Slide 67: Multi comparison One barometer vs all the rest

## Slide 68: Multi comparison One barometer vs all the rest

## Slide 69: Multi comparison One barometer vs all the rest
Sometimes negative, sometimes positive correlation?

## Slide 70: Multi comparison One barometer vs all the rest
Temperature peaks not in sync at the end.

## Slide 71: Multi comparison One barometer vs all the rest
This one is still good.

## Slide 72: Multi comparison One barometer vs all the rest

## Slide 73: Multi comparison One barometer vs all the rest

## Slide 74: Multi comparison One barometer vs all the rest
Old but also still good.

## Slide 75: Multi comparison One barometer vs all the rest

## Slide 76: Multi comparison One barometer vs all the rest

## Slide 77: Multi comparison One barometer vs all the rest

## Slide 78: Multi comparison One barometer vs all the rest

## Slide 79: Multi comparison One barometer vs all the rest

## Slide 80: Multi comparison One barometer vs all the rest

## Slide 81: Multi comparison One barometer vs all the rest
Very old but still “OK”? The oscillations are not all that big. Why?

## Slide 82: Multi comparison One barometer vs all the rest

## Slide 83: Multi comparison One barometer vs all the rest

## Slide 84: Multi comparison One barometer vs all the rest
Where will it end?

## Slide 85: Multi comparison One barometer vs all the rest
What happened?

## Slide 86: Multi comparison One barometer vs all the rest
Calibration test could verify this one is too low currently?

## Slide 87: Multi comparison One barometer vs all the rest
This one “was” new? Now unstable?

## Slide 88: Multi comparison One barometer vs all the rest
Unstable?

## Slide 89: Multi comparison One barometer vs all the rest
Unstable?

## Slide 90: Multi comparison One barometer vs all the rest
Unstable?

## Slide 91: Multi comparison One barometer vs all the rest
Unstable?

## Slide 92: Multi comparison One barometer vs all the rest
Unstable?

## Slide 93: Multi comparison: remarks
Universal way of matching barometers on timestamps.
  Truncation: 12h
    E.g. observation at 2019-02-02 13:05:00 UTC is truncated to 2019-02-02 12:00:00 UTC
  Averaging over truncated values.
Missing values for barometers are a potential problem.
  E.g. for 2020, if there is no barometers available for comparison, or if there is only a limited number of barometers available?
Seems many barometers become sensitive to temperature changes after x years?
  No clear temperature dependence pattern.
Many barometers seem broken? Median assumes about 50 % non-broken.
  After BAOL1XX less drifting cases but more unstable cases?
Some are just unstable? (i.e. not drifting)
  Mostly BAOL5XX

## Slide 94: Next steps
Continue “multi-comparison” analysis?
  Try removing altitude-effect for better comparison? (e.g. remove and )
    Compare altitudes based on barometric formula with real elevation based on the coordinates
  …?
First algorithm: detect trend for some structural break at for model
  detect_drifts(x, other)
    Need enough “other” data to compute “x”. Problem: what is enough?
    Detect any significant change in trend after .
  detect_drifts(x)
    Can be based on apriori data about . If trend is larger than the worst case in apriori data, then flag from .
  detect_drifts(x, altitude)
    …?

## Slide 95: Next steps: potential problems
How certain are we that barometers from analysis 04 are broken?
  Need a validated set of drifting and non-drifting barometers to make comparisons of algorithms.
Unstable barometers: detecting change after with is difficult.

## Slide 96: Questions?
Frederic: question from GitHub solved?
Frederic: “Typically one Barologger can cover a radius of 30 km (20 mile) and/or every 300 m (1000 ft) elevation change.”
  Radius 30 km: error SD increase with 0,3 cmH2O (analysis)
  Elevation change of 300 m: 36 cmH2O change in mean (barometric formula)
Piet: hydrostatic error: 2 cmH2O.
  For baro’s from analysis of median: 1,3 cmH2O
  After about 100km the error is also 2 cmH20 due to distance.
Piet: -20 tot 50 °C: effect?
  Effect based on analysis: 70 * 0,068 = 4,8 cmH2O

## Slide 97: The End